## Slide 1: Applying HLS to FPGA Data Preprocessing in the Advanced Particle-astrophysics Telescope
Presenter: Meagan Konst
Advisor: Roger Chamberlain

## Slide 2: Agenda
Introduction
Background and Related Work
Accelerated Algorithms
HLS Implementation
Conclusion and Future Work
Q+A Session

## Slide 3: Introduction

## Slide 4: APT Overview

## Slide 5: APT Overview
Goal: Capture cosmic rays and tell devices on Earth where to look to collect additional data

## Slide 6
APT Hardware Pipeline
Wavelength-shifting Fibers
ALPHA ASICs
ADC BUFFER
FPGA
CPU

## Slide 7
Input Data Generation
Originally Developed by Gary’s Group, modified and fleshed out by Marion with data models from the Italian group

## Slide 8
Input Data Packet
2 ADC Buffer Banks, A sample is collected every 10 ns, one Bank can be read while the other is filled, sent to the FPGA when a trigger occurs

## Slide 9: Data Preprocessing
Pedestal: Constant Capacitive Noise of an ADC Buffer Slot
  Pedestal Subtraction
Integral: Sum of a signal over time to collect total energy produced by an event

## Slide 10: Integral Types
Trigger
Key: Blue: Pre-Signal Noise Purple: Main Signal Green: Tail Red: Whole Window
ADC Counts
Time

## Slide 11: Background and Related Work

## Slide 12: FPGA Design Approaches
Hardware Description Languages (HDLs)
  Steep Learning Curve
  Prone to User Error
  Difficult to Debug
High-Level Synthesis (HLS)
  Allows Software Engineers to program FPGAs using software languages such as C/C++ and OpenCL C

## Slide 13: Related Work
HLS Portability from Intel to Xilinx –Zhili Xiao
  Naïve Porting required lots of modifications and had terrible performance
  Lots of optimization techniques applied and still not as performant
Transformations of High-Level Synthesis Codes for High-Performance Computing –Johannes de Fine Licht
  Gave a 3.5 hr talk on current best practices and iterative optimization techniques for improving performance

## Slide 14: Vitis Host and Kernel
Host
Create an OpenCL Environment
Initialize Inputs as Memory Buffers
Run the kernel
Read and Process Outputs
Kernel
FPGA Module where algorithms are implemented
Communicates with Host over a specified interface (AXI for now)
Notes: AXI: Advanced eXtensible Interface, ARM bus-protocol

## Slide 15: Loop Types
Imperfect
Semi-Perfect
Perfect
Similar Performance

## Slide 16: Imperfect Loops
for (variable bounds) {
operations
for (variable bounds) {
operations
}
operations
}
Operations outside innermost loop
Variable Loop Bounds

## Slide 17: Semi-Perfect Loops
for (variable bounds) {
for (constant bounds) {
operations
}
}
Variable loop bounds in only the outermost loop

## Slide 18: Perfect Loops
for (constant bounds) {
for (constant bounds) {
operations
}
}
Can Require Conditional Execution in the innermost loop

## Slide 19: Accelerated Algorithms

## Slide 20: SW Interface Functions
data_packet_dat_to_struct
peds_dat_to_arrays
write_output
  write_header
  write_integrals
struct_to_json
  add_to_json
  add_samples_to_json
(Host)

## Slide 21
SW Interface Functions
data_packet_dat_to_struct
HW
peds_dat_to_arrays
struct_to_json
write_output
output.txt
packet.json
integrals
EventStream.dat
peds.dat
all_peds
data_packet
data_packet

## Slide 22: data_packet_dat_to_struct
EventStream.dat
(input)
Functionality: Takes generated input signals and produces a data_packet struct

## Slide 23: data_packet_dat_to_struct
SW_Data_Packet
(output)
Functionality: Takes generated input signals and produces a data_packet struct

## Slide 24: peds_dat_to_arrays
peds.dat
(input)
Functionality: Takes generated pedestal values and produces a 3D array of them

## Slide 25: peds_dat_to_arrays
SAMPLE NUMBER
SAMPLE NUMBER
CHANNEL NUMBER
CHANNEL NUMBER
(data structure)
Functionality: Takes generated pedestal values and produces a 3D array of them

## Slide 26: peds_dat_to_arrays
(output)
Functionality: Takes generated pedestal values and produces a 3D array of them

## Slide 27: write_output
output.txt
Header Info
Integrals
(output)
Functionality: Takes header information, integrals, and their bounds and produces a text file

## Slide 28: struct_to_json
packet.json
(output)
Functionality: Takes data_packet struct and creates a JSON file for debugging purposes / data dump

## Slide 29: HW Functions
ped_subtract
  Removes pedestal noise through subtraction
integral
  Takes an integral over a specified time interval whose bounds are trigger-relative
(Kernel)

## Slide 30: ped_subtract
0
255
0
255
SAMPLES
PEDESTALS
Starting Sample Number
0
255
RESULTS
-
Executed for all 16 Channels, 256 Samples Each

## Slide 31: integral
start
end
start
end
OR
+
+
+
+
+
+
+
+
Executed for all 16 Channels
Bounds are Trigger-Relative
ped_subtract results
ped_subtract results

## Slide 32: HLS Implementation

## Slide 33: Compilation Times
sw_emu: ~1min
  Functional Correctness
hw_emu: ~30min
  Cycle Accuracy
hw: ~3hr
  Place and route -> bitstream

## Slide 34: Performance Goals
Frequency
Latency
Area
Power

## Slide 35: Main Statistics Collected
Timing Information
  Target Frequency: 300 MHz
  Estimated Frequency: 411 MHz
Latency Information (Goal: 2.56 μs)
  Cycles and Seconds
  Best, Average, and Worst
Area Information
  Counts and Percent Utilization
  FF, LUT, DSP (not used), BRAM, URAM (not used)
  ASIC Count Estimate (Goal: 12)
Power Consumption (Only Available from HW Runs)
Notes: Explain Target / Estimated Frequency, Define Abbreviations, say explicitly that fewer resources is better

## Slide 36: Disclaimers
Experiments were conducted on the CloudLab u280 board (UltraScale)
Percent Utilization Numbers were calculated for our target board (XC7K325T-2FFG900C) (Kintex-7)
Samples and Pedestals are both stored in external memory (HBM)
Reported Statistics are for the entire Kernel

## Slide 37: Iterations
Naïve Approach
Added Tripcount Numbers
ped_subtract optimizations
  Attempt to Fix Memory Access Issue
  Semi-Perfect ped_subtract loop
  Perfect ped_subtract loop
integral optimizations
  Forced Perfect integral loop
  Perfect integral loop with combined logic
  Perfect integral loop with ternary operators
  Attempted to Remove False Dependence
  Removed False Dependence with proper temp buffer

## Slide 38: Naïve Approach
Warnings: Memory Port Contention in ped_subtract and integral loop could not be flattened
Latency: No numbers since loops had variable bounds
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
14853 | 3.644 | 39600 | 12.14 | 66 | 0.4120 | 8
Vitis

## Slide 39: Naïve Approach
Ran on the CloudLab Machine (u280)
Clock Frequency: 286 MHz
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
21416 | 5.254 | 10309 | 3.161 | 25 | 0.1561 | 19
HW Run
Average Power Consumption (W)
10.591
Cycles | Time | Times Slower Than Goal
84370 | 0.295 ms | 115

## Slide 40: Added Tripcount Numbers
Undefined Iterations -> Worst-case Iterations
Set min=1 and max=256 (NUM_SAMPLES)
Same Warnings and Numbers
Cycles | Time | Times Slower Than Goal
40533 | 0.135 ms | 53

## Slide 41: ped_subtract optimizations

## Slide 42: Attempt to Fix Memory Access Issue
Accessed data_packet fields once instead of on each loop iteration
Did not resolve Memory Warnings
The numbers remained the same

## Slide 43: Semi-Perfect ped_subtract loop
Resolved Memory Warnings for ped_subtract
Moved pedestal indexing logic to the innermost loop
Semi-Perfect because outermost loop still has variable (data_packet->samples_to_be_read) bounds
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
10278 | 2.522 | 22753 | 6.978 | 52 | 0.3246 | 14
Cycles | Time | Times Slower Than Goal
42582 | 0.142 ms | 55

## Slide 44: Perfect ped_subtract loop
Made an assumption that we will always read the full memory buffer (256 samples)
Gives us more accurate latency numbers (no longer need Tripcount pragma) but not much change otherwise
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
10261 | 2.517 | 22737 | 6.973 | 52 | 0.3246 | 14

## Slide 45: integral optimizations

## Slide 46: Disclaimer
Integral is assumed to have variable bounds
If the bounds were constant, a different optimization approach would be taken

## Slide 47: Forced Perfect integral loop
Before
if
for
for
else
for
for
for
After
for
for
if
if
if
else
if
Notes: Conditions: BEFORE: if (end >= start) {} else {} AFTER: if (NUM_SAMPLES idx = 0) {initialize} if (end >= start) {if (within those bounds)} else {if (within those bounds)}

## Slide 48: Forced Perfect integral loop
II=137!!! Exploded, did NOT map well without further optimizations / re-arranging
Memory Violations on Integral ports now
Takes up much less space, but is ridiculously slow
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
4648 | 1.140 | 7097 | 2.176 | 24 | 0.1498 | 45
Cycles | Time | Times Slower Than Goal
2331359 | 7.770 ms | 3035

## Slide 49: Perfect integral loop with combined logic
Before
for
for
if
if
if
else
if
After
for
for
if
if
Notes: Conditions: AFTER: if (NUM_SAMPLES idx = 0) {initialize} if (within bounds) {accumulate}

## Slide 50: Perfect integral loop with combined logic
Consolidated if-else statements into one if condition
Did not resolve warnings
Same Latency Numbers, Took up less space
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
4517 | 1.108 | 6965 | 2.136 | 24 | 0.1498 | 46

## Slide 51: Perfect integral loop with ternary operations
Replaced if statements with ternary operations
Did not resolve warnings
Slight improvement in Latency and Area
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
4468 | 1.096 | 6987 | 2.143 | 24 | 0.1498 | 46
Cycles | Time | Times Slower Than Goal
2314699 | 7.715 ms | 3014

## Slide 52: Attempted to Remove False Dependence
Functionally Incorrect! Labeled a True Dependence as False
I created a temporary variable but not a temporary buffer, need both (WAR dependence)
Resolved Warnings
Latency significantly improved, using more FFs than LUTs
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
7140 | 1.752 | 6432 | 1.973 | 24 | 0.1498 | 50
Cycles | Time | Times Slower Than Goal
21499 | 71.656 μs | 28

## Slide 53: Removed False Dependencies with proper temp buffer
This approach requires a temporary buffer that is written to the output at the end of execution
Functionally Correct
Huge hit to Area
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
8242 | 2.022 | 18821 | 5.772 | 52 | 0.3246 | 17
Cycles | Time | Times Slower Than Goal
21382 | 71.266 μs | 28
Vitis

## Slide 54: Removed False Dependencies with proper temp buffer
Ran on the CloudLab Machine (u280)
Clock Frequency: 280 MHz
Much Slower than predicted in hw_emu
Also takes up less area than predicted
FFs | % Util | LUTs | % Util | BRAM | % Util | ASICs
14058 | 3.449 | 6817 | 2.091 | 22 | 0.1373 | 28
HW Run
Average Power Consumption (W)
8.639
Cycles | Time | Times Slower Than Goal
87640 | 0.313 ms | 122

## Slide 55: Conclusion and Future Work

## Slide 56: Naïve vs. Current Approach
Naïve Approach
Integral Loop Iterations: Dependent on Integral Bounds
Less Latency
More Area
More Power
Current Approach
Integral Loop Iterations: 256 per Channel
More Latency, but not as much of an increase as would be expected due to iteration increase
Less Area
Less Power

## Slide 57: Conclusion
Naïve Approach took a fair amount of re-arranging to get something Vitis-compatible and functionally correct
Applying HLS Optimizations is not straightforward
  Main Issues:
    Memory Port Contention
    Functional Correctness when applying pragmas
    Trade-off between Latency and Area
Perfect Loops are just the starting point for HLS Optimization

## Slide 58: Future Work
Create custom variable types to get more accurate numbers
Bitmasks
Dataflow Pipeline
Vectorization
Memory Burst Accesses
Add Other Algorithms to FPGA
  Centroiding
  Zero Suppression
  Multi-event detection
  Data Compression
Use Vitis HLS to create an IP that can be treated as a black box

## Slide 59: Q+A Session
Notes: If we put the pedestals in BRAM, it’ll be 2x16x256x12 = 98,304 bits -> 96 Kb so with current model -> 0.7366 % Utilization so not the bottleneck